Flambe Controller Spec
Revision 54
# 1. Specification
## 1.1 Connection Overview

Figure 1: Hardware Overview
## 1.2 States

System Logical States
State	Relay 1 / Pilot Valve (Igniter)	Relay 2 / Main Valve (Sparkler)	Relay 3	Fan
Error	Off	Off	Off	Off
Off	Off	Off	Off	Off
Idle	On	Off	On	Off
On	On	On	On	Possibly On

Table 1: Logical States
## 1.3 State Machine

Figure 2: State Diagram

State Transition Table
Controller Input		Current → Next State
Name	Code	Error...	Off...	Idle...	On...
Low	L	Off	Off	Off	Off
Medium	M	Off	Off	Idle	Idle
High	H	Error	On	On	On
No Signal	N	Error	Error	Error	Error

Table 2: State Transitions

## 1.4 Input PWM Signal
### Timings
The Arduino detects the input signal based on timing the period between the rising and falling edge of the input PWM signal:
Input Signal Timings
Lower Bound (microseconds)	Upper Bound (microseconds)	Signal
0	500	NoSignal
500	1300	Low
1300	1700	Medium
1700	2500	High
2500	∞	NoSignal

Table 3: PWM Timings
### Hysteresis
In order to prevent the input signal from rapidly changing when the input in near to a boundary, hysteresis is performed. The input signal length must be more than 100 microseconds outside the current input band in order for the input to change. This value can be changed by editing the HYSTERESIS definition in the sketch. Hysteresis is not applied when the current signal is NoSignal.
### Error Rejection
The system state may only enter On or Error states if three matching inputs are received in a row. This is to prevent very short errors from triggering state changes. Repeated inputs are not required to enter other states, so the system will immediately turn off on the first Low input. The number of repeated inputs required can be changed by editing the sketch definitions ON_REPEATS and ERR_REPEATS.
### No Signal Handling
NoSignal state is detected using the Arduino millis() function. Whenever a rising edge is detected both the microsecond and millisecond times are recorded. The falling edge interrupt checks the microsecond time, and the main loop checks the millisecond time. If the last recorded rising edge was over 100 milliseconds ago, the input state is changed to NoSignal. This timeout can be changed by editing the TIMEOUT definition in the sketch. This implementation does not rely on timers or resets.
If the input signal is present but the timing falls in the NoSignal ranges, the state machine switches to Error state immediately.
Once in Error state, High inputs are ignored and the state can only transition to Off if Low or Medium are received.
## 1.5 Output PWM Signal for Relays
Output is generated by the Arduino Servo library. Since it controls servos, it accepts an input in the range 0 to 180 degrees. The values required to switch relays on and off seems to be around 45 degrees for off and 135 degrees for on. These values can be changed in the sketch by editing the defines R_OFF and R_ON.
## 1.6 Output PWM Signal for Fan
Output is again generated by the Arduino Servo library. The fan has variable speed control and takes into account the raw input PWM signal timing in addition to the current system state. If the system state is not On then the fan should never spin and the output PWM signal will be set to F_OFF. If the state is On then the output signal depends on the input PWM timing. If it is less than or equal to F_THRESH then the output will be F_OFF. If greater, the output will be scaled from F_MIN when the input is F_THRESH to F_MAX when the input is the upper bound of the High trigger bound.

Figure 3: Fan PWM Curve
## 2 Reference
## 2.1 Arduino Pro Micro Pin Out

Figure 4: Arduino Pro Micro Pinout
Only pins marked with a tick can be used as PWM outputs. Any pin may be used as a PWM input. Pin 10 was selected as input because it is easy to locate on the board.
## 2.2 Arduino IDE Setup
### Permissions
Ensure you have added your user to the dialout group:
sudo gpasswd -a <user> dialout
Note: In order to activate the new group you must start a new login session.
### Dependencies
To install required dependencies, click Tools → Library Manager. Search for the dependency and then click Install.
Note: If the Library Manager option is not present, it means your IDE version is too old.
The following dependencies are required:
1. PinChangeInterrupt
2. Servo *

Dependencies marked * should be installed by default with the Arduino IDE.

### Target Board
Use Tools → Board → Arduino Leonardo as the target board type. This is a 5V board based on Atmega32U4, with the same logical pin mapping as Pro Micro.
### Serial Monitor
The serial monitor is opened by clicking Tools → Serial Monitor. In older versions of the IDE, uploading a sketch will close the serial monitor.
Whenever the Arduino resets, the serial monitor will lose some of the first messages. This is because the USB device disconnects and reconnects, and the IDE must reopen it. This may cause the initial “Reset” message to be lost.
# 3. Testing
## 3.1 Direct Connection Test
Figure 5: Direct Connection Setup
1. Connect Any relay directly to the output of the RC receiver.
2. Verify that moving the transmitter to ‘H’ turns on the relay.
3. Verify that moving the transmitter to ‘L’ turns off the relay.

## 3.2 Input Test
Figure 6: Input Test Setup
1. Program passthrough sketch to the Arduino.
2. Connect the RC receiver to pin 10 of the Arduino.
3 Open the Arduino Serial Monitor.
4. Verify that moving the transmitter trigger to ‘H’ causes the Arduino to output ‘Input: High’.
5. Verify that moving the transmitter trigger to ‘M’ causes the Arduino to output ‘Input: Medium’.
6. Verify that moving the transmitter trigger to ‘L’ causes the Arduino to output ‘Input: Low’.
7. Disconnect the receiver and verify that the Arduino prints “Input: NoSignal” repeatedly.

## 3.3 Output Test
Figure 7: Output Test Setup
1. Program File → Examples → Servo → Sweep to the Arduino
2. Connect any relay to the Arduino pin 9.
3. Verify that the relay turns on and off approximately every 2.7 seconds. (2.7s on, 2.7s off.)
## 3.4 Pass-through Test
Figure 8: Pass-Through Test Setup
1. Program passthrough sketch to the Arduino.
2. Connect the RC receiver to pin 10 of the Arduino.
3. Connect any relay to pin 9 of the Arduino.
4. Verify that moving the transmitter trigger to ‘H’ causes the relay to turn on.
5. Verify that moving the transmitter trigger to ‘L’ causes the relay to turn off.
6. Move the relay to Arduino pin 3 and repeat steps 4 and 5.
7. Move the relay to Arduino pin 5 and repeat steps 4 and 5.
8. Move the relay to Arduino pin 6 and repeat steps 4 and 5.